## Slide 1
Assessment of climate change impacts on semi-arid watersheds in Peru
1 Department of Agricultural and Biological Engineering, Purdue University, West Lafayette, IN, United States
2 Department of Agronomy, Purdue University, West Lafayette, IN, United States
3 School of Computer Science, Universidad Nacional de San Agustín, Arequipa, Peru
* Email: fdaneshv@purdue.edu
Fariborz Daneshvar1*, Indrajeet Chaubey1, Laura Bowling2, Keith Cherkauer1, Andre Moraes1, Jose Herrera3
MOTIVATION
OBJECTIVES
STUDY AREA
HYDROLOGIC MODELING
CLIMATE SECENARIOS
RESULTS
Hydrologic Model Performance
Current Condition
Future Scenarios
Low seasonal precipitation and high demand for water use
High spatial variation in precipitation (Figure 1)
Need for water regulation and diversion to mitigate impact of future climate variations
Figure 1. Average annual precipitation (mm) in the region (2008-2017)
Develop hydrological model to simulate water cycle
Evaluate hydrologic response to climate change
Quilca-Vitor-Chili River Basin in Arequipa in Peru
Area: 13,549 km2
Major City: Arequipa (population of over 850,000)
Four reservoirs for water regulation
Two water diversions from Camana River Basin
One water withdrawal for irrigation project
Figure 2. Major rivers, water bodies, and water regulations in Quilca-Vitor-Chili River Basin
water diversion from Camana River Basin
water diversion from Camana River Basin
water withdrawal for irrigation project
Soil and Water Assessment Tool (SWAT)
Physically based, semi-distributed watershed/water quality model
SWAT Inputs layers:
(3.a) Topography (12.5 m)
Figure 3. SWAT input layers
(3.d) Sub-watersheds (205)
(3.e) Rivers (205)
(3.b) Land cover (1:600,000)
(3.c) Soil (10 km)
SWAT Inputs Databases:
1) Daily climate (precipitation and temperature) for 15 stations
2) Point source discharges (2 points) and withdrawal (1 point)
3) Reservoirs daily release rates
NASA Earth Exchange Global Daily Downscaled Projections (NEX-GDDP)
General Circulation Model (GCM) runs conducted under the Coupled Model Intercomparison Project Phase 5 (CMIP5)
Resolution: 0.25 degrees (-25 km * 25 km)
Three climate models: 1) CNRM-CM5, 2) MPI-ESM-MR, 3) MRI-CGCM3
Two Representative Concentration Pathways (RCPs): 1) 4.5, 2) 8.5
Two periods of simulations: 1) Near future (2010-2039), 2 Far future (2040-2069)
Chart: Monthly flow (m3/s)
| 39814 | 39845 | 39873 | 39904 | 39934 | 39965 | 39995 | 40026 | 40057 | 40087 | 40118 | 40148 | 40179 | 40210 | 40238 | 40269 | 40299 | 40330 | 40360 | 40391 | 40422 | 40452 | 40483 | 40513 | 40544 | 40575 | 40603 | 40634 | 40664 | 40695 | 40725 | 40756 | 40787 | 40817 | 40848 | 40878 | 40909 | 40940 | 40969 | 41000 | 41030 | 41061 | 41091 | 41122 | 41153 | 41183 | 41214 | 41244
Observed | 8.941 | 11.48 | 15.11 | 10.77 | 7.374 | 10.85 | 9.603 | 7.469 | 7.328 | 8.483 | 9.746 | 7.221 | 8.237 | 14.16 | 8.318 | 8.958 | 12.02 | 11.88 | 8.815 | 10.89 | 11.48 | 11.77 | 12.96 | 9.866 | 12.933 | 39.153 | 33.856 | 26.682 | 10.714 | 13.522 | 13.036 | 13.003 | 12.617 | 15.775 | 19.978 | 9.705 | 38.1373 | 132.8962 | 40.1839 | 32.9797 | 11.4361 | 13.3347 | 12.6861 | 11.3026 | 15.6133 | 17.5084 | 15.0433 | 21.3455
SWAT | 8.973 | 35.49 | 49.78 | 41.93 | 15.91 | 8.281 | 7.435 | 6.942 | 7.17 | 5.406 | 3.673 | 4.919 | 6.475 | 14.76 | 19.82 | 13.34 | 10.14 | 9.378 | 9.754 | 5.073 | 5.133 | 6.603 | 11.18 | 7.907 | 9.906 | 39.95 | 44 | 36.56 | 16.8 | 12.62 | 9.054 | 4.579 | 4.507 | 4.954 | 11.15 | 9.634 | 54.4 | 83.35 | 66.02 | 52.73 | 22.94 | 13.73 | 5.462 | 2.585 | 6.726 | 8.053 | 8.058 | 15.32
Figure 4. SWAT model calibration
SWAT model calibrated for 2009-2013
Calibration point: Charchani station
Model performance:
NSE: 0.53
PBIAS: -3.79 %
R2: 0.58
CONCLUSIONS
Figure 5. Daily average of surface runoff (mm) and water yield (mm) at sub-watershed level for current condition (2009-2017)
Figure 6. Ensemble average of daily water yield (mm) at sub-watershed level
Slight increase in surface runoff and water yield are predicted in high attitude headwaters, especially for RCP 8.5 in far future (2040-2069)
All models predicted low water supply in low altitude catchments
Incorporation of water diversions and withdrawals into future simulations will provide more accurate picture of water availability and will be subject of future research
Arequipa city
Charchani station
Poster #EP53F-1960
Funding for this work provided by the Arequipa Nexus Institute for Food, Energy, Water and the Environment through the Universidad Nacional de San Agustín, Arequipa Peru